## Slide 1: Motion Exercise 1
Positioning

## Slide 2: Device used: 4 SIM. 10-01 and Inputs and Outputs

## Slide 3
MACHINE_CONTROL
CONVEYOR_CONTORL
CUTTER_CONTOL

## Slide 4: Generic Axis

## Slide 5: Function Block : Generic Axis and PLCopen used
VAR:
  power_GA : MC_Power;
  home_GA : MC_Home;
  move_velocity_GA : MC_MoveVelocity;
  move_additive_GA : MC_MoveAdditive;
  move_position_GA : MC_MoveAbsolute;
  status_GA : MC_ReadStatus;
  position_GA : MC_ReadActualPosition;
  reset_GA : MC_Reset;
  read_axis_error_GA :MC_ReadAxisError;
  old_command : STRING[80];
  mc_stop_GA : MC_Stop;
  old_velocity : REAL;
Inputs:
  velocity
  acceleration
  axis_enable
  axis_command
  distance
  axis_address
  position
  direction
Outputs:
  actual_position
  axis_error
  error_id
  axis_state
  command_executed

## Slide 6: Generic Axis States
READY
POWERED
WAIT_POWER
NOT_POWERED
IN_VELOCITY_STATE
MOVE_POSITION_STATE
MOVE_ADDITIVE_STATE
MOVE_VELOCITY_STATE
STOPPING

## Slide 7: Machine Variables

## Slide 8: Machine States
OFF_STATE (*the system is off*)
CONFIRM_INIT (*Wait to be powered*)
CONVY_MV_STATE (*running state and waits for a triggered state or be turned off*)
SENSOR_DETECT (*the system has been triggered and is getting ready for the cutting action*)
CUTTING_STATE (*the system performs the cut and gets ready to go back to running state*)
FAULT_STATE (Fault either in Conveyor axis or Cutter axis )

## Slide 9: Machine workflow
Start button
CONFIRM_INT
NOT Conv init
NOT Cutt init
CONVY_MV_STATE
White_Button
SENSOR_DETECT
CONVY_MV_STATE
activate_cut
SENSOR_DETECT
NOT conv_stop
CUTTING_STATE
NOT activate_cut
OFF_STATE

## Slide 10: Conveyor Variables

## Slide 11: Conveyor States
OFF_STATE_CONVEYOR (*Off state*)
INIT_AXIS (*Initialization of the general axis*)
CONFIRM_CONV_MV (*Enabling of the axis relative to the conveyor*)
CONV_MOVING_STATE (*Initialization of the movement of the conveyor and relative variables*)
CONV_STOPED, (*Stopping of the movement of the conveyor and setting of the relative variables*)
AXIS_ENABLED
FAULT_STATE_CONVETOR
(Fault either in Conveyor axis or Cutter axis )

## Slide 12: Conveyor workflow(Master)
Conv init
INIT
AXIS
OFF STATE
NOT axis_enabled
AXIS ENABLED
move_conv
CONFIRM_CONV_MV
Cmd_exct
CONV_MOVING_MV
Conv_stop
CONV_STOPED

## Slide 13: Cutter Variables

## Slide 14: Cutter States
INIT_AXIS (*Initialization of the general axis*)
AXIS_ENABLED (*Enabling of the axis relative to the conveyor*)
CUTTER_MV_DOWN
CUTTER_MV_UP
OFF_STATE (*Off state*)
FAULT_STATE_CUTTER

## Slide 15: Cutter workflow(slave)

## Slide 16: CAM PROFILE

## Slide 17: Error Management
MACHINE_CONTROL:
    IF(ConveyorError OR CutterError) THEN
    FAULT := TRUE;
    stop_machine := TRUE;
    MACHINE_STATE:= FUALT_STATE;
    END_IF;
CONVEYOR_CONTORL:
  IF(FAULT) THEN
  axis_command := ‘STOP’;
  conveyor_state := FUALT_STATE_CONVEYOR;
  END_IF;
CUTTER_CONTOL:
  IF(FAULT) THEN
  axis_command := ‘STOP’;
  cutter_state := FUALT_STATE_CUTTER;
  END_IF;